## Slide 1
KONCEPTUĀLA SHĒMA
Ierobežota INFORMĀCIJA
4x riteņu Platforma
Polaris RZR-XP 1000
Drive-by-Wire Kit
Polaris RZR-XP 1000
PowerDistributionDatasheet
Kontrolē:
Stūri
Bremzes
Gāzo
Ātrumkārbu
ZED One cam
ZED Box 16GB
Orin NX
Endpoint controller 1002
SRC Pro 1002 Fort
Standard BLE & ISM Radio 868 MHz 100-200m line of sight
15m-30m line of sight (BLE)
FAKRA Z type connector 2x
2x 5 m
DBW ROS2 driver
Joystic demo
CAN protocol (23-pin connector)
BLE
GMSL2
GPS RTK U-Blox ZED-F9P
GNSS multiband antenna (SMA conn.)
5G router
MAVLINK msg
USB
Stream
Mavlink enc/dec
Video stream
5G network
PPTP tunel
ZED X (stereo)
StereoLabs camera
Telemetry UGV
USB-CAN module (dataspeed)
USB
CAN
5G router
HOST PC (GC) with HW video decoding
MAVLINK msg
Video streaming
Polaris-1
Polaris-2
172.25.64.194
172.25.65.12
MAVLINK msg
TAK server
MAVLINK msg

## Slide 2: ROS2 arhitektūra GC (workspace)
mavlink libs and c++ headers
gc_gui package (python)
mavros_joystic package (c++)
mavros_telemetry_proc
package (c++)
scripts
folder (bash)
cpp_mono_stream_rx
cpp app (c++)
cpp_stereo_stream_rxcpp app (c++)
ros2 joy package (c++)
/joy msg
mavros_joystic
node
joy_node
node
172.25.65.12:14550
mavlink msgs
ugv_telemetry_proc
node
localhost:14551
mavlink msgs
gui_node
node
/ugv/telemetry_freq msg
/ugv/telemetry_state msg
172.25.65.12:5002
udp video stream
172.25.65.12:5004
udp video stream
run.sh
Desktop shortcut
runs
runs
run.xml
launch script
Microphone Audio
gst-streamer
runs
localhost:5008
udp audio stream
Defines: Telemetry.msg & Freq.msg
5G router
USB JOY
GC OS

## Slide 3: ROS2 arhitektūra Polaris (workspace)
mavlink libs and c++ headers
mavros_commutator
package (c++)
polaris_joystick
package (c++)
mavros_ugv_telemetry
package (c++)
scripts
folder (bash)
cpp_mono_streamer
cpp app (c++)
cpp_stereo_streamer cpp app (c++)
dbw_ros
(c++)
CAN-USB module
joy_polaris
node
172.25.116.22:14552
TAK mavlink msgs
mavros_ugv_telemetry
node
172.25.64.194:14551
GC mavlink msgs
mavros_commutator
node
localhost:5002
udp video stream
localhost:5004
udp video stream
run.sh
run.xml
launch script
Microphone Audio
gst-streamer
/vehicle/vehicle_velocity
msg
5G router
DataSpeed commutator
UGV devices
joyReader_node
node
gearMonitor_node
node
enableJoy_node
node
*Watch_node
nodes
/vehicle/* msgs
USB
runs
runs
/vehicle/gear/report msg
localhost:14550
GC mavlink msgs
/joy_polaris msg
Ctrl msgs
polaris.service
Linux OS
run.xml
launch script
runs
runs
gps_reader
package (python)
gps_reader_node
node
GNSS reciever
/ugv/gps/fix msg
runs
172.25.64.194:5008
udp audio stream
polaris.service
UGV
ZED BOX OS

## Slide 4: Setup GC on Ubuntu 24.04
Install ROS2 KILTED KAIJU (ubuntu 24.04):
Use link: Ubuntu (deb packages) — ROS 2 Documentation: Kilted documentation
Create ROS2 workspace:
mkdir –p ~/gc_ws/src
cd gc_ws
Init the workspace:
colcon build --symlink-install
source install/setup.bash
Clone LMT GC repository:
cd src/
git clone git@github.com:dainissilamikelis/polaris-ground-control.git
cd polaris-ground-control
git submodule update --init --recursive
Build mavlink:
cd polaris-ground-control/mavlink
cmake -Bbuild -H. -DCMAKE_INSTALL_PREFIX=~/gc_ws/install/mavlink -DMAVLINK_DIALECT=common -DMAVLINK_VERSION=2.0
cmake --build build --target install
Compile ROS2 workspace’s packages:
cd ~/gc_ws
source install/setup.bash
sudo rosdep init
rosdep update
source install/setup.bash
colcon build --symlink-install
Setup Python tools:
sudo apt install python3-kivy
Setup other tools:
sudo apt install wmctrl
CUDA 13.0 (must be compared to the version of host machine):
  wget https://developer.download.nvidia.com/compute/cuda/repos/ubuntu2404/x86_64/cuda-keyring_1.1-1_all.deb
  sudo dpkg -i cuda-keyring_1.1-1_all.deb
  sudo apt-get update
  sudo apt-get -y install cuda-toolkit-13-0
Create desktop shortcut to run GC:
Edit ~/gc_ws/src/polaris-ground-control/scripts/run.sh to set correct environment path
Edit ~/gc_ws/src/polaris-ground-control/scripts/ GroundControlPolaris.desktop to set the correct path to run.sh script
chmod +x ~/gc_ws/src/polaris-ground-control/scripts/run.sh
cp ~/gc_ws/src/polaris-ground-control/scripts/ GroundControlPolaris.desktop ~/Desktop
chmod +x ~/Desktop/GroundControlPolaris.desktop
Allow Launching for the shortcut (Mouse Right - > Allow Launching)

## Slide 5: Setup Polaris ZED Orion NX 16GB on Ubuntu 22.04 (1)
Check system:
lsb_release –a
dpkg-query -W nvidia-l4t-core
nvidia-smi
apt-cache show nvidia-jetpack
Original version of Orion NX 16GB: is R36 (release), REVISION: 3.0 - > JetPack 6.0 & L4T Version 36.3.0
Install ROS2 Humble: Ubuntu (deb packages) — ROS 2 Documentation: Humble documentation
Generate ssh key for the project repositories and register it in github.com (for a user):
ssh-keygen -t ed25519 -C „user-e-mail-here“
Install ZED StereoLabs cameras SDK (ZED SDK 5.0, CUDA 12.6, Jetpack 6.2 )
More info: here
mkdir -p pol_ws/downloads && cd pol_ws/downloads
wget -O ZED_SDK_Tegra_L4T36.3_v5.0.7.zstd.run "https://download.stereolabs.com/zedsdk/5.0/l4t36.3/jetsons?_gl=1*1bezr7q*_gcl_au*MTIwNTg0MDg0Mi4xNzU2Mjg3
Mzcx“
chmod +x ./ZED_SDK_Tegra_L4T36.3_v5.0.7.zstd.run
ZED_SDK_Tegra_L4T36.3_v5.0.7.zstd.run
# Installation path: /usr/local/zed/samples/
Install ZedLink drivers: (drivers list)
download deb file: stereolabs-zedbox-duo_1.3.1-LI-MAX96712-all-ZEDBOX-L4T36.3.0_arm64.deb
sudo dpkg -i ./stereolabs-zedbox-duo_1.3.1-LI-MAX96712-all-ZEDBOX-L4T36.3.0_arm64.deb
sudo reboot
sudo dmesg | grep zedx
Install ZED gstreamer libraries:
Install prereqirements from here
git clone https://github.com/stereolabs/zed-gstreamer.git
cd zed-gstreamer
mkdir build && cd build
cmake -DCMAKE_BUILD_TYPE=Release ..
make
sudo make install
sudo apt update
sudo apt install libgstrtspserver-1.0-dev
Check the prev. install:
gst-inspect-1.0 zedsrc
gst-inspect-1.0 zedxonesrc
gst-inspect-1.0 zeddemux
gst-inspect-1.0 zeddatamux
gst-inspect-1.0 zeddatacsvsink
gst-inspect-1.0 zedodoverlay
Connect and test the camera (useful info):
sudo systemctl restart zed_x_daemon
ZED_Diagnostic -c

## Slide 6: Setup Polaris ZED Orion NX 16GB on Ubuntu 22.04 (2)
Init ROS2 WS:
cd ~/pol_ws
mkdir src
colcon build
Clone LMT Polaris repository:
cd src
git clone git@github.com:dainissilamikelis/polaris-os.git
cd polaris-os
git submodule update --init --recursive
Build mavlink:
cd mavlink
cmake -Bbuild -H. -DCMAKE_INSTALL_PREFIX=~/pol_ws/install/mavlink -DMAVLINK_DIALECT=common -DMAVLINK_VERSION=2.0
cmake --build build --target install
touch COLCON_IGNORE
Install depences:
sudo apt update
sudo apt install ros-humble-can-msgs
cd ~/ros2_ws/src
git clone https://bitbucket.org/DataspeedInc/dataspeed_can.git
cd ..
rosdep install --from-paths src --ignore-src -r -y
colcon build --packages-select dataspeed_can_msg_filters
cd src
git clone https://github.com/autowarefoundation/ros2_socketcan.git
cd ..
rosdep install --from-paths src --ignore-src -r –y
colcon build --packages-select ros2_socketcan ros2_socketcan_msgs
Setup CAN-USB dataspeed tool device:
lsusb
echo 'SUBSYSTEM=="usb", ATTR{idVendor}=="6923", ATTR{idProduct}=="0112", MODE="0666"' | \
sudo tee /etc/udev/rules.d/99-dataspeed-can.rules
sudo udevadm control --reload-rules
sudo udevadm trigger
ls /dev | grep can
modprobe can
modprobe can_raw
modprobe can_dev
ip link show
Setup GNNS receiver: ZED link
sudo apt install libgps-dev
cgps -s
Compile ROS2 workspace’s packages:
cd ~/pol_ws
source install/setup.bash
sudo rosdep init
rosdep update
source install/setup.bash
colcon build --symlink-install
Register as service
Edit ~/pol_ws/ polaris-os/scripts/polaris.service to set correct run.sh path and user name, and working dir
Edit ~/pol_ws/ polaris-os/scripts/run.sh to set CG IP address
sudo cp ~/pol_ws/src/polaris-os/scripts/polaris.service /etc/systemd/system
chown user:user /home/user/pol_ws/src/polaris-os/scripts/run.sh
chmod +x /home/user/pol_ws/src/polaris-os/scripts/run.sh
sudo systemctl daemon-reexec
sudo systemctl daemon-reload
sudo systemctl enable polaris.service
sudo systemctl start polaris.service
Check status:
sudo systemctl status polaris.service
journalctl -u polaris.service

## Slide 7: RUN commands (manual run)
Polaris ZED Box (user@admin): 172.25.65.12
Bash Terminal 1:
cd ~/pol_ws
source install/setup.bash
ros2 launch polaris_joystick joystick.launch.xml
Bash Terminal 2:
cd ~/pol_ws
source install/setup.bash
ros2 launch mavros_commutator run.xml
Bash Terminal 3:
cd ~/pol_ws
source install/setup.bash
./build/ZED_Streaming_Sender/ZED_Streaming_Sender 5002
Bash Terminal 4:
cd ~/pol_ws
source install/setup.bash
./build/ZED_One_live/ZED_One_streaming_sender 5004
CG hos (sholc@sholc): 172.25.64.194
Bash Terminal 1:
cd ~/gc_ws
source install/setup.bash
ros2 run gc_gui gui_node
Bash Terminal 2:
cd ~/gc_ws
source install/setup.bash
ros2 run mavros_telemetry_proc mavros_telemetry_proc_node
Bash Terminal 3:
cd ~/gc_ws
source install/setup.bash
ros2 launch mavros_joystic run.xml
Bash Terminal 4:
cd ~/gc_ws
source install/setup.bash
./build/ZED_One_live/ZED_One_streaming_receiver 172.25.65.12:5004
Bash Terminal 5:
cd ~/gc_ws
source install/setup.bash
./build/ZED_Streaming_Receiver/ZED_Streaming_Receiver 172.25.65.12:5002